## Slide 1: ECE 260C Logic Synthesis
Cho Moon

## Slide 2: Bio
Cho Moon has over 25 years of experience in EDA. He is currently a distinguished engineer at Precision Innovations. He has led advanced node development for tools like PrimeTime, Fusion Compiler and First Encounter at Synopsys, Blaze DFM, Cadence and other EDA and semiconductor companies.
He has expertise in static timing analysis, pre-route and post-route optimization, Engineering Change Order (ECO) optimization, logic synthesis and formal verification.
He holds a PhD from UC Berkeley. Bob Brayton was his advisor.

## Slide 3: Bob Brayton’s Favorite Quote
Your manuscript is both good and original. Unfortunately, the part that is good is not original, and the part that is original is not good.
    Samuel Johnson
Prof. Bob Brayton

## Slide 4: Outline
Introduction
Two-level Logic Synthesis
Multi-level Logic Synthesis
  Classical
  Contemporary
Technology Mapping
  Classical
  Contemporary

## Slide 5: Why Logic Synthesis?
Indispensable
  Problem is too hard without it
  Similar to C++/C compilers
Big impact on final PPA (performance, power and area)
Foundation for many applications like
  Verification
  Timing analysis
  Testing
  Sequential optimization
Notes: Logic synthesis is a necessary foundation for logic optimization and verification/test. As P&R tools evolve with stronger resynthesis functionality to meet tighter PPA goals, the need for sound logic synthesis only increases.

## Slide 6: Design Flow
System Specification
RTL
Logic synthesis
Technology mapping
Physical synthesis
Manufacturing
ABC
Verification
Where does logic synthesis fit in?
Yosys
ABC
OpenROAD
Notes: Yosys works to elaborate and synthesize a technology mapped netlist from RTL that OpenROAD can then place and route. Both utilize ABC.
Yosys calls into ABC to perform logic optimization and technology mapping, while Yosys itself handles RTL elaboration and a large set of structural transformations, such as hierarchy flattening or adder synthesis. OpenROAD uses ABC to perform physical resynthesis, providing ABC with STA timing data.
https://github.com/The-OpenROAD-Project/OpenROAD/tree/master/src/rmp

## Slide 7: Synthesis Example (Yosys + ABC)
module adder1 (
input clk,
input a,
input b,
input cin,
output reg sum,
output reg cout
);
reg [1:0] result;
always @(posedge clk) begin
result <= a + b + cin;
sum <= result[0];
cout <= result[1];
end
endmodule
module adder1(clk, a, b, cin, sum, cout);
wire _0_;
wire _1_;
input a;
wire a;
input b;
wire b;
input cin;
wire cin;
input clk;
wire clk;
output cout;
wire cout;
wire \result[0] ;
wire \result[1] ;
output sum;
wire sum;
sky130_fd_sc_hd__xor3_1 _2_ ( .A(cin), .B(a), .C(b), .X(_1_) );
sky130_fd_sc_hd__maj3_1 _3_ ( .A(cin), .B(a), .C(b), .X(_0_) );
sky130_fd_sc_hd__dfxtp_1 \cout$_DFF_P_ ( .CLK(clk), .D(\result[1] ),.Q(cout) );
sky130_fd_sc_hd__dfxtp_1 \result[0]$_DFF_P_ ( .CLK(clk), .D(_1_),.Q(\result[0] ) );
sky130_fd_sc_hd__dfxtp_1 \result[1]$_DFF_P_ ( .CLK(clk), .D(_0_), .Q(\result[1] ) );
sky130_fd_sc_hd__dfxtp_1 \sum$_DFF_P_ ( .CLK(clk), .D(\result[0] ), .Q(sum) );
endmodule
RTL (Register Transfer Level) Specification
= “Behavioral” Verilog
Gate-level Netlist Implementation
= “Structural” Verilog

## Slide 8: Problem
Given
  Initial design
  Design constraints
    Timing
    Power
    Area
  Target technology libraries
Produce
  Optimal gate-level netlist that meets design constraints
Very hard optimization problem!

## Slide 9: Adder Choices
Slide Courtesy of Martin Poviser and Emil Tywoniak at YosysHQ
Area vs. delay tradeoff for different adders with varying bit widths
Notes: Synthesis of large inferred structures, like the adders demonstrated here (but also multipliers or memories), demonstrate the breadth of the solution space that synthesis can address. Power, Performance, and Area tradeoffs need to be accounted for.

## Slide 10: Combinational Logic Synthesis
Slide courtesy of Devadas, et. al
Logic Synthesis
netlist
netlist
Library
tech
independent
tech
dependent
2-level
Logic opt
multilevel
Logic opt
Library

## Slide 11: Boolean Functions
f(x) : Bn B
B = {0, 1}, x = (x1, x2, …, xn)
x1, x2, … are variables
x1, x1, x2, x2, … are literals
each vertex of Bn is mapped to 0 or 1
the onset of f is a set of input values for which f(x) = 1
the offset of f is a set of input values for which f(x) = 0

## Slide 12: Logic Formulas
Slide courtesy of Devadas, et. al
Notes: A cube (diagrammed) represents a product (AND) of inputs.

## Slide 13: Logic Representation
Binary decision diagram (BDD)
Logic Network (LN)
And-inverter Graph (AIG)
F | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1
abcd | 0000 | 0001 | 0010 | 0011 | 0100 | 0101 | 0110 | 0111 | 1000 | 1001 | 1010 | 1011 | 1100 | 1101 | 1110 | 1111
Sum of products (SOP): F= ab + cd
Product of sums (POS): F = (a+c)(a+d)(b+c)(b+d)
Truth Table (TT)
Slide Courtesy of Alan Mischenko
Notes: Optimizing logic can be done on these graph representations (BDD, LN, AIG). AIGs scale the best to larger logic. Balancing an AIG as a tree can be thought of as improving timing. Minimizing number of nodes correlates to lower area.

## Slide 14: Which Representation and Which Optimization?
Design Size | # Inputs | Representation | Optimization | Tools
Small | <= 16 | Truth Table (TT) Sum of Products (SOP) | Minimize number of products or literals ab is better than abc ab is better than abc + abc’ | Espresso
Medium | 16-100 | Binary Decision Diagrams (BDD) Logic Network (LG) And-inverter Graph (AIG) | Minimize number of nodes or widths Minimize “area” or levels Minimize number of nodes or levels | SIS VIS, MVSIS ABC
Large | > 100 | And-inverter Graph (AIG) | Minimize number of nodes or levels | ABC
Slide Courtesy of Alan Mischenko

## Slide 15: Historical Perspective
Slide Courtesy of Alan Mischenko

## Slide 16: Outline
Introduction
Two-level Logic Synthesis
Multi-level Logic Synthesis
  Classical
  Contemporary
Technology Mapping
  Classical
  Contemporary

## Slide 17: Two-level Logic Synthesis Problem
Given an arbitrary logic function in two-level form, produce a smaller representation.
For sum-of-products (SOP) implementation on PLAs (programmable logic arrays), fewer product terms and fewer inputs to each product term mean smaller area.
  O1 = I1 I2 + I1’ I2’
  O2 = I1’ I2’
I1
I2
O1
O2

## Slide 18: Sum-of-products (SOP)
A function can be represented by a sum of cubes (products):
  f = ab + ac + bc
Since each cube is a product of literals, this is a “sum of products” representation
A SOP can be thought of as a set of cubes F
  F = {ab, ac, bc} = C
A set of cubes that represents f is called a cover of f.
  F={ab, ac, bc} is a cover of f = ab + ac + bc.

## Slide 19: Prime Cover
A cube is prime if there is no other cube that contains it
  (for example, b c is not a prime but b is)
A cover is prime iff all of its cubes are prime
c
b
a

## Slide 20: Irredundant Cube
A cube c of a cover C is irredundant if C fails to be a cover if c is dropped from C
A cover is irredundant iff all its cubes are irredundant (for example, F = a b + a c + b c)
c
b
Not covered
a

## Slide 21: Quine-McCluskey Method
We want to find a minimum prime and irredundant cover for a given function.
  Prime cover leads to min number of inputs to each product term.
  Min irredundant cover leads to min number of product terms.
Quine-McCluskey (QM) method (1960’s) finds a minimum prime and irredundant cover.
  Step 1: List all minterms of on-set: O(2^n) n = #inputs
  Step 2: Find all primes: O(3^n) n = #inputs
  Step 3: Construct minterms vs primes table
  Step 4: Find a min set of primes that covers all the minterms: O(2^m) m = #primes

## Slide 22: QM Example
F = a’ b’ c’ + a b’ c’ + a b’ c + a b c + a’ b c
Find a minimum set of primes that covers all the minterms
  “Minimum column covering problem”
 | b’ c’ | a b’ | a c | b c
a’ b’ c’ | X |  |  | 
a b’ c’ | X | X |  | 
a b’ c |  | X | X | 
a b c |  |  | X | X
a’ b c |  |  |  | X
Essential primes

## Slide 23: ESPRESSO – Heuristic Minimizer
Quine-McCluskey gives a minimum solution but is only good for functions with small number of inputs (< 10)
ESPRESSO is a heuristic two-level minimizer that finds a “minimal” solution
    ESPRESSO(F) {
    do {
    reduce(F);
    expand(F);
    irredundant(F);
    } while (fewer terms in F);
    verfiy(F);
    }

## Slide 24: ESPRESSO ILLUSTRATED
Reduce
Irredundant
Expand

## Slide 25: Outline
Introduction
Two-level Logic Synthesis
Multi-level Logic Synthesis
  Classical
  Contemporary
Technology Mapping
  Classical
  Contemporary

## Slide 26: Multi-level Logic Synthesis
Two-level logic synthesis is effective and mature
Two-level logic synthesis is directly applicable to PLAs and PLDs
But…
There are many functions that are too expensive to implement in two-level forms (too many product terms!)
Two-level implementation constrains layout (AND-plane, OR-plane)
Rule of thumb:
  Two-level logic is good for control logic
  Multi-level logic is good for datapath or random logic

## Slide 27: Multi-level Logic Synthesis Problem
Given
  Initial logic network
  Design constraints
    Arrival times, required times, power consumption, noise immunity, etc…
  Target technology libraries
Produce
  a minimum “cost” netlist consisting of the gates from the target libraries such that design constraints are satisfied

## Slide 28: Modern Approach to Logic Optimization
Divide logic optimization into two subproblems:
  Technology-independent optimization
    determine overall logic structure
    estimate costs (mostly) independent of technology
    simplified cost modeling
  Technology-dependent optimization (technology mapping)
    binding onto the gates in the library
    detailed technology-specific cost model
Orchestration of various optimization/transformation techniques for each subproblem
Slide courtesy of Keutzer

## Slide 29: Network Representation
Logic Network:

## Slide 30: Node Representation: Sum of Products (SOP)
Example:
abc’+a’bd+b’d’+b’e’f (sum of cubes)
Advantages:
  easy to manipulate and minimize
  many algorithms available (e.g. AND, OR, TAUTOLOGY)
  two-level theory applies
Disadvantages:
  Not representative of logic complexity. For example,
    f=ad+ae+bd+be+cd+ce
    f’=a’b’c’+d’e’
    These differ in their implementation by an inverter.
  hence not easy to estimate logic; difficult to estimate progress during logic manipulation

## Slide 31: Technology-Independent Optimization
Technology-independent optimization is a bag of tricks:
  Two-level minimization (also called simplify)
  Constant propagation (also called sweep)
    f = a b + c; b = 1 => f = a + c
  Decomposition (single function)
f = abc+abd+a’c’d’+b’c’d’ => f = xy + x’y’; x = ab ; y = c+d
  Extraction (multiple functions)
f = (az+bz’)cd+e g = (az+bz’)e’ h = cde

f = xy+e g = xe’ h = ye x = az+bz’ y = cd

## Slide 32: More Technology-Independent Optimization
More technology-independent optimization tricks:
  Substitution
  g = a+b f = a+bc
  
  f = g(a+c)
  Collapsing (also called elimination)
  f = ga+g’b g = c+d
  
  f = ac+ad+bc’d’ g = c+d
  Factoring (series-parallel decomposition)
f = ac+ad+bc+bd+e => f = (a+b)(c+d)+e

## Slide 33: Outline
Introduction
Two-level Logic Synthesis
Multi-level Logic Synthesis
  Classical
  Contemporary
Technology Mapping
  Classical
  Contemporary

## Slide 34: Motivation for Contemporary Synthesis
Classical combinational tech-independent synthesis
  suboptimal
  complicated
  hard to implement
  slow
What if we replace it with something that is
  suboptimal, but
  simple
  easy to implement
  fast
Slide Courtesy of Alan Mischenko & Bob Brayton
Notes: Contemporary methods look to apply a similar set of logic optimizations but with logic representations that are more amenable to large scales.

## Slide 35: And-Inverter Graph (AIG)
Every node is two-input AND
Dotted line denotes inversion
Primary inputs and register outputs at bottom
Primary outputs and register inputs at top
Can represent any set of logic functions
Slide Courtesy of Alan Mischenko & Bob Brayton
Notes: And-Inverter Graphs are the most common logic representation and are used by Berkeley ABC, an open-source synthesis system.
https://people.eecs.berkeley.edu/~alanmi/abc/

## Slide 36: Logic Network vs. AIG
Equivalent AIG in ABC
a
b
c
d
f
e
x
y
z
Logic network in SIS
a
b
c
d
e
x
y
f
z
AIG is a logic network of 2-input AND nodes and inverters (dotted lines)
Slide Courtesy of Alan Mischenko & Bob Brayton

## Slide 37: One AIG Node – Many Cuts
Combinational AIG
a
b
c
d
f
e
AIG can be used to compute many cuts for each node
  Each cut in AIG represents a different SIS node
  No a priori fixed boundaries
  Implies that AIG manipulation with cuts is equivalent to working on many logic networks at the same time
Different cuts for the same node
Slide Courtesy of Alan Mischenko & Bob Brayton
Notes: Cuts are a necessary part of logic synthesis, particularly in technology mapping. Each cut can represent a standard cell or FPGA LUT in the target technology.
Each possible cut (which can be animated through in the slides) represents a new logic network (seen in the previous slide). The benefit of the AIG is that it separates this cut generation process from the rest of the logic optimization process rather than explicitly encoding cuts in its structure.

## Slide 38: k-Feasible Cuts
Definition. A set of nodes C is a k-feasible cut for a node n if
(1) all the paths from the primary inputs (PIs) to node n pass through at least one node in C,
(2) the number of nodes in C does not exceed k
k | Average number of cuts per node
4 | 6
5 | 20
6 | 80
7 | 150
3-feasible cuts of n:
C1 = { p, k }
C2 = { a, b, s }
Not 3-feasible cuts of n:
C3 = { p, b, c }
C4 = { a, b, s, c }
n
p
k
a
b
s
c
PIs: a, b, c
Slide Courtesy of Alan Mischenko & Bob Brayton
Notes: A k-feasible cut is a cut with a certain number of maximum nodes.

## Slide 39: AIG Structural Hashing
Leads to a compact representation
Is applied during AIG construction
  Propagates constants
  Makes each node structurally unique
Slide Courtesy of Alan Mischenko & Bob Brayton
Notes: Structural hashing (referred to as strash-ing in ABC and related papers) aims to introduce a “partially canonical” form to the AIG by replacing redundant logic with a single instantiation of logic. This reduces the number of nodes in the AIG, which can allow more cuts to be explored. Canonical forms of logic can speed up technology mapping further by allowing for faster matching i.e. the canonical AIG of a possible technology cell and the canonically AIG of a behaviorally-equivalent cut of a design’s logic network should be the same.
See more details here: https://people.eecs.berkeley.edu/~alanmi/publications/2005/tech05_fraigs.pdf

## Slide 40: AIG Resubstitution
Resubstitution considers a node in a logic network and expresses it using a different set of fanins
X
X
Notes: Resubstitution over a node tries to express the same behavior of that node using different fan-ins. These fan-ins can be primary inputs, outputs of existing nodes, or outputs of new nodes. Resubstitution may be referred to by the number of nodes it is allowed to add to the network (e.g. 0-resub, 1-resub, ..., N-resub).
The goal of resubstitution can be different i.e. to reduce the number of nodes (correlating with area), improve the balance of the tree (correlating with timing), more detailed estimated cost (timing/power/area) of nodes (based on some early techmapping), etc.
See a (non-AIG) example here: https://msoeken.github.io/papers/2020_date.pdf

## Slide 41: AIG “speedup”
Timing Criticality
Critical nodes
  Used by many traditional algorithms
Critical edges
  Used by ABC
ABC pre-computes critical edges of critical nodes
  Reduces computation
An edge between critical nodes may not be critical
  See illustration: edge 13
1
2
3
4
4
3
2
1
Primary inputs
Primary outputs

## Slide 42: Delay-Oriented Restructuring
Using traditional MUX-restructuring
  AKA generalized select transform
x and y are the critical edge inputs

## Slide 43: AIG Rewriting
Pre-computing subgraphs
  Consider function f = abc
a
b
a
c
Subgraph 1
b
c
a
Subgraph 2
a
c
b
Subgraph 3
Rewriting subgraphs
Rewriting node A
Rewriting node B

a
b
a
c

a
b
a
c
A
Subgraph 1
b
c
a
A
Subgraph 2
b
c
a
B
Subgraph 2
a
b
a
c
B
Subgraph 1
In both cases 1 node is saved
Slide Courtesy of Alan Mischenko & Bob Brayton

## Slide 44: Combinational Synthesis By AIG Rewriting
iterate 10 times {
for each AIG node {
for each k-cut
derive node output as function of cut variables
if ( smaller AIG is in the pre-computed library )
rewrite using improved AIG structure
}
}
Note: each AIG node has, on average, 5 4-cuts compared to a SIS node with only 1 cut
Rewriting at a node can be very fast – using hash-table lookups, truth table manipulation, disjoint decomposition
Slide Courtesy of Alan Mischenko & Bob Brayton

## Slide 45: Experimental Results (MCNC)
Slide Courtesy of Alan Mischenko & Bob Brayton
A. Mischenko, S. Chatterjee, R. Brayton, “DAC-Aware AIG Rewriting: A Fresh Look at Combinational Logic Synthesis”, DAC 2006

## Slide 46: Outline
Introduction
Two-level Logic Synthesis
Multi-level Logic Synthesis
  Classical
  Contemporary
Technology Mapping
  Classical
  Contemporary

## Slide 47: Technology-Dependent Optimization
Technology-dependent optimization consists of
Technology mapping: maps logic network to a set of gates from technology libraries
Local transformations
  Discrete resizing
  Cloning
  Fanout optimization (buffering)
  Logic restructuring
Slide courtesy of Keutzer

## Slide 48: Classical Technology Mapping
Input
  Technology independent, optimized logic network
  Description of the gates in the library with their cost
Output
  Netlist of gates (from library) which minimizes total cost
General Approach
  Construct a subject DAG for the network
  Represent each gate in the target library by pattern DAG’s
  Find an optimal-cost covering of subject DAG using the collection of pattern DAG’s
  Canonical form: 2-input NAND gates and inverters
DAGON: Technology Binding and Local Optimization by DAG Matching
(K. Keutzner, 1987)
Notes: https://ieeexplore.ieee.org/document/1586250

## Slide 49: DAG Covering
DAG covering is an NP-hard problem
Solve the sub-problem optimally
  Partition DAG into a forest of trees
  Solve each tree optimally using tree covering
  Stitch trees back together
Slide courtesy of Keutzer
Notes: Divide and conquer over the DAG

## Slide 50: Tree Covering Algorithm
Transform netlist and libraries into canonical forms
  2-input NANDs and inverters
Visit each node in BFS from inputs to outputs
  Find all candidate matches at each node N
    Match is found by comparing topology only (no need to compare functions)
  Find the optimal match at N by computing the new cost
    New cost = cost of match at node N + sum of costs for matches at children of N
  Store the optimal match at node N with cost
Optimal solution is guaranteed if cost is area
Complexity = O(n) where n is the number of nodes in netlist

## Slide 51: Tree Covering Example
into the technology library (simple example below)
Find an ``optimal’’ (in area, delay, power) mapping of this circuit
Slide courtesy of Keutzer

## Slide 52: Library Gates
INVERTER 2
NAND2 3
NAND3 4
NAND4 5
Element/Area Cost
Tree Representation (normal form)
Slide courtesy of Keutzer

## Slide 53: Trivial Covering
subject DAG
7 NAND2 (3) = 21
5 INV (2) = 10
Area cost 31
Slide courtesy of Keutzer
Can we do better with tree covering?

## Slide 54: Optimal Covering
``subject tree’’
INV 2
ND2 3
2 ND3 8
AOI21 4
Area cost 17
AOI21
ND2
INV
ND3
ND3
Slide courtesy of Keutzer

## Slide 55: Summary of Classical Technology Mapping
DAG covering formulation
  Separated library issues from mapping algorithm (can’t do this with rule-based systems)
Tree covering approximation
  Very efficient (linear time)
  Applicable to wide range of libraries (std cells, gate arrays) and technologies (FPGAs, CPLDs)
Weaknesses
  Problems with DAG patterns (Multiplexors, full adders, …)
  Large input gates lead to many patterns

## Slide 56: Outline
Introduction
Two-level Logic Synthesis
Multi-level Logic Synthesis
  Classical
  Contemporary
Technology Mapping
  Classical
  Contemporary

## Slide 57: AIG Technology Mapping
Input: A logic network (And-Inverter Graph)
Output: A netlist of K-LUTs implementing AIG and optimizing some cost function
The subject graph
The mapped netlist
Technology
Mapping
a
b
c
d
f
e
a
b
c
d
e
f

## Slide 58: Sample ABC Scripts
Area Optimization Script | 
Command | Function
strash | transform combo logic into AIG by "structural hashing"
dch | similar to &dch decompose to AND-INV and tech map subject to timing constraints
map –B 0.9 | perform std cell mapping of the current network using 2-level logic minimization approach (Boolean matching + resynthesis) -B 0.9 delay multiplier to bias gate selection (0.0 = area mode, 1.0 = delay mode)
topo | rearrange nodes to be in topological order for STA
stime –c | perform STA using liberty library
buffer –c | perform buffering and sizing on mapped network
upsize –c | selectively increase gate sizes on the critical path
dnsize –c | selectively decrease gate sizes while maintaining delay
Delay Optimization Script |  | 
Command | Repeat | Function
&get –n | X1 | convert current network into GIA (generalized-iterative-and)
&st |  | perform structural tech map by considering physical layout
&dch |  | decompose to AND-INV and tech map subject to timing constraints
&nf |  | perform tech mapping of the network using network flow algorithm
&st | X5 | perform structural tech map by considering physical layout
&syn2 |  | perform secondary delay/area opt subject to timing constraints
&if –g –K 6 |  | perform FPGA tech map based on priority cuts
&synch2 |  | perform 2nd stage sequential opt including retiming and clock gating
&nf |  | perform tech mapping of the network using network flow algorithm
&put | X1 | put current network into memory buffer
buffer –c |  | perform buffering and sizing on mapped network
topo |  | rearrange nodes to be in topological order for STA
stime –c |  | perform STA using liberty library
upsize –c |  | selectively increase gate sizes on the critical path
dnsize –c |  | selectively decrease gate sizes while maintaining delay

## Slide 59: Comparison of Classical vs. AIG Synthesis
Slide Courtesy of Alan Mischenko & Bob Brayton

## Slide 60: Thank You